RP2040-PICO30
User Manual
Rev.1.0	May 2023	olimex.com
# Introduction to RP2040-PICO30

RP2040-PICO30 is re-design of the popular Raspberry PI RP2040-PICO board with these improvements:
- all 30 RP2040 GPIOs are available to the user
- USB-C power supply connector which allow more current to be used by the board
- SY8089A 3.3V 2A (3A peak) DCDC power supply
- 2MB or 16MB Flash versions are possible
- RESET button is add
- Four layer board for better noise immunity and USB differential pair routing
- UEXT connector (pUEXT 1.0 mm step connector)
- Dimensions 21x51 mm

RP2040-PICO30 keep same layout and pinout as original RP2040-PICO.
The original RP2040-PICO exposes only 26 out of the 30 RP2040 GPIOs this sometimes is not good and RP2040-PICO30 solves this issue.

+ Important notice: RP2040-PICO30 keep same pinout as RP2040-PICO because in latter there are 8 GND connections. RP2040-PICO30 connects the four missing GPIOs: GPIO23, GPIO24, GPIO25, GPIO29 on GND pins PIN13. PIN18. PIN23, PIN28. When you use RP2040-PICO30 on RP2040-PICO board make sure these GPIOs are INPUTS!
## Order codes for RP2040-PICO30 and accessories:

RP2040-PICO30	industrial grade RP2040-PICO board with 30 GPIOs exposed
RP2040-PICO-30U	RP2040-PICO30 with UEXT, LED, R10, R15, R16
RP2040-PICO30-16	RP2040-PICO30 with 16MB of Flash (max possible for RP2040)
RP2040-PICO-30U-16	RP2040-PICO30 with 16MB of Flash, UEXT, LED, R10, R15, R16

# HARDWARE

## RP2040-PICO30 layout:

RP2040
UEXT connector with SPI I2C UART

PIN.40
PIN.21

Flash

USB-C

DEBUG

LED

LED enable jumper
RESET button
PIN.20

Boot button
PIN.1

## RP2040-PICO30 GPIOs:

POWER SUPPLY:

VBUS	+5V fro, USB-C output
VDD_SYS	+5V may be output or input
if you want to use as input i.e. to feed power from external 5V to this line make sure	board is not connected to USB!
when you use as output i.e. you feed external electronics from it up to 1A @ 5V
+3.3V	output which can source up to 2A @ 3.3V
3V3_EN	input, when pulled to GND stops the 3.3V DCDC convertor

GPIOs:

GPIO23	PIN.28 this GPIO is missing in the original RP2040-PICO and on this place there is
GND so if you use RP2040-PICO30 in RP2040-PICO design make sure it’s	initialized as INPUT
GPIO24	PIN.23 this GPIO is missing in the original RP2040-PICO and on this place there is	GND so if you use RP2040-PICO30 in RP2040-PICO design make sure it’s initialized	as INPUT
GPIO25	PIN.18 this GPIO is used for LED drive in the original RP2040-PICO and on this	place there is GND so if you use RP2040-PICO30 in RP2040-PICO design make sure	it’s initialized as INPUT
GPIO29	PIN.13 this GPIO is missing in the original RP2040-PICO and on this place there is	GND so if you use RP2040-PICO30 in RP2040-PICO design make sure it’s initialized	as INPUT
## RP2040-PICO30 schematics:

RP2040-PICO30 latest schematic is on GitHub

## UEXT connector:

UEXT connector stands for Universal EXTension connector and contain +3.3V, GND, I2C, SPI, UART signals.
UEXT connector can be in different shapes.
The original UEXT connector is 0.1” 2.54mm step boxed plastic connector. All signals are with 3.3V levels.

As the boards become smaller and smaller some smaller packages were introduced too beside the original UEXT connector
- mUEXT is 1.27 mm step boxed header connector which is with same layout as UEXT
- pUEXT is 1.0 mm single row connector (this is the connector used in RP2040-PICO30)

Olimex has developed number of MODULES with this connector. There are temperature, humidity, pressure, magnetic field, light sensors. Modules with LCDs, LED matrix, Relays, Bluetooth, Zigbee, WiFi, GSM, GPS, RFID, RTC, EKG, sensors and etc.

## pUEXT signals:

# SOFTWARE:

RP2040-PICO30 uses same software as RP2040-PICO
- Raspberry PI C-SDK
- MicroPython SDK
# Revision History
Revision 1.0 May 2023